## Slide 1: EPICS and Software
K. Alexander Fahey
LLRF Electrical Engineer
EIC LLRF Controls-ASR-PDR2
April 21st & 22nd, 2026

## Slide 2: Charge Questions
Have the committee recommendations from the Preliminary Design Review been addressed adequately?
Are the system requirements sufficiently defined, understood, and documented for this phase of the design?
Do the designs meet the requirements?
Are the interfaces sufficiently defined, understood and documented for this phase of the design?
Are the analysis, simulations, drawings and specifications, and work plans, sufficient for this phase of the design?
Are the plans to address ES&H and quality sufficient for this phase of the design?
Have technical risks been identified and are mitigation plans adequate for this phase of the design?
Is the overall design maturity sufficient to proceed with the final design phase?

## Slide 3: Recommendations and Comments Addressed
EIC # | Recommendation | Action Taken
1049 | Provide a complete hardware, firmware, and software test suite to support development and testing across all aspects of RF System development | Designs for daughtercard, interfaces, and EPICS IOC tracked on EIC GitHub
1051 | Embed software engineer/s in the RF Systems development team to begin developing EPICS IOCs and tools for RF System Controls, and data migration from the LLRF application to the IOC | An electrical engineer in RF Controls has made progress on developing IOCs for RF System Controls
Charge #1
# | Comment | Action Taken
8 | An EPICS software engineer should be identified as soon as possible | An EPICS software engineer is developing IOCs for RF System Controls

## Slide 4: Outline
Scope
Design Flow
Technical Progress
Software Block Diagram
EPICS Lessons Learned
QC Plan
Path Forward
Summary

## Slide 5: Software Scope
EPICS uses IOCs (Input-Output Controllers) to modify device parameters
  Controls WBS provides EIC groups with baseline environments
  We need to develop IOCs for the devices we deploy
Certain software functions will be migrated between RHIC and EIC
  Would be inefficient to re-invent the wheel with these algorithms
Charge #2, 4

## Slide 6: Common Platform
Timing/Data Link
Inputs
Machine parameters
Cavity voltages & status
Ring h=1 NCO phases
Beam measurements (radius, etc.)
Outputs
frev FTW
Ref NCO phases
System events/triggers
RF signals
Inputs
Beam phase
Reference line
Outputs
Reference line drive
Debug / monitoring
Real-time CPUs
Beam control loops
  Output frev, φs
Ring2ring synchro/cogging
Injection cogging
Beam permit high-level logic
Digital signals
Outputs
Beam permit status
Debug / monitoring triggers
Debug / monitoring status
FPGA core & application blocks
NCO/DDS with soft reset
Digital down converter
Cavity vector sum calc
Beam sync event generator
Beam permit logic
EPICS IOC Control
Packets generated and interpreted by PscDrv on A53 core
Charge #4

## Slide 7: Design Flow – Vitis
FWFWK Workflow
  Git tracking, scripts for compilation
Automatically pulls in bitstream from hardware project
Compiler environment can be scripted
  Adding specific libraries
  Defining target CPU
  Defining environment variables
Binary files are automatically created and exported
  No need for Vitis GUI
DesyRDL generates headers for EPICS functionality
  Defined through configurable jinja2 templates
  Current template automates PSCDrv PVs
Charge #1, 2, 4
[TALK #10 Mai]

## Slide 8: Design Flow – EPICS
EIC Requires EPICS
  Migrating from current ADO framework
  Open-Source
  Large Install Base
PSCDrv - Advantages
  Portable Streaming Controller Driver
  Carrier to Remote IOC communication
  Lower overhead on carrier than running full IOC
  Carrier does not need specific firmware to handle each daughtercard
IOC VMs
  Running common EPICS binary on a shared drive
[TALK #6 Mernick]
Charge #1, 2, 4
Notes: Carrier does not need specific software
Requ

## Slide 9: Design Flow – DesyRDL Templates
Jinja2 template structure
Automates file creation
  Takes in RDL Parameters
  Outputs mapped registers
Several filetypes built-in
  Vivado AXI mapping
  Vitis C header
Can create custom filetypes
  EPICS .db file
Hooks into DESY FWFWK
  Registers do not need to be manually updated to be controlled by PscDrv
Integrates into AXI Chip2Chip
  Carrier can read and write data in these defined registers
VHDL Block
C Header
EPICS PV
RDL Register
Charge #1, 2, 4
Notes: Add DesyRDL to

## Slide 10: Design Flow – Build Environment
Virtual Machine (VM) Based
  Remotely controlled over EIC network
  Provided by Controls Group
  VMs configured for FWFWK compilation
  VMs configured for EPICS IOC compilation
Remote JTAG Debug
  Physical machine access not required for debugging
Standardized Workflow
  All processing is remote
  Local machines not required to run Linux (FWFWK requirement)
Charge #2

## Slide 11: Software Block Diagram

## Slide 12: Technical Progress – Algorithm Porting
Program DSP core ported from RHIC Virtex-5 to R5 core of EIC CP Carrier
  Calculates revolution frequency from ADO beam parameters and Update Link beam status
ADO parameters moved to EPICS PSCDrv parameters
EPICS IOC running on remote VM
Live run data pulled from RHIC Update Link during final run
  Running calculations matched current and historical data
Charge #1, 2, 5
Notes: Details of Program DSP

## Slide 13: Technical Progress – LLRF Digitizer
Remote IOC Controlling LLRF Digitizer
  PscDrv packets between CPC and IOC
  CPC reads/writes from shared memory
Phoebus UI for IOC
  Generic get/set UI (top)
  Formatted controller UI (bottom)
Charge #1, 2, 5
Notes: Put length of test

## Slide 14: Technical Progress – LLRF Digitizer
Successfully Logged Digitizer Readback PVs
  Entire Test data captured
    March 10-24, 2026
  Both slow data and snapshot data are logged
Charge #1, 2, 5
Cavity Voltage (~ 220 kV)
Cavity Phase (100 degrees)
24.6MHz Loopback
Raw Data
I
Q
IQ After Low-Pass Filter
CP LLRF Test with RHIC 197 MHz Cavity

## Slide 15: EPICS Lessons Learned
Large number of resources available for learning
  USPAS courses readily available
Scripting PVs for large register maps important
  Changes to map can shift many addresses
  Manually shifting PV addresses tedious and time-consuming
Charge #1, 2, 6
[TALK #6 Mernick]
Notes: EPICS is well documented
Grammar of second bullet point

## Slide 16: QC Plan
Developing on local copy of IOC
  Confirming PVs work as expected before uploading to IOC server
    EPICS is verbose with PV errors
  Confirming Phoebus UI looks as expected
Git tracked IOC changes
  Significant changes can be monitored
  IOC revision can be rolled back for older digitizer firmware
Charge #1, 6

## Slide 17: Path Forward and Summary
Path Forward
  We are continuing to test the digitizer on a test setup in LLRF lab
  Modifications to the IOC are being made to add required EPICS modules from Controls
  Work is being done to port more LLRF algorithms for tests in RF Test Facility
We have made significant progress in EPICS development
  LLRF Digitizer is EPICS controlled
We are migrating RHIC algorithms to Common Platform
  Program DSP has been migrated to Common Platform
We are ready to support an EPICS-controlled EIC, using Common Platform hardware
Questions?
Charge #8
Notes: Bring waveform to digitizer