## Slide 1: Application Layer & Operator Interfaces
Kunal Shroff
Software Technical Lead
EIC Accelerator Controls Global Software, Networking & Computing PDR
June 15-17, 2026

## Slide 2: About Me – Kunal Shroff
I am the Controls Software Technical Lead for the Electron-Ion Collider (EIC) at Brookhaven National Laboratory, where I lead the architecture and deployment strategy for controls software and operational services.
I have 17 years of experience developing control systems software for large scientific facilities and serve as the technical lead of the EPICS Phoebus Collaboration, an international effort developing next-generation tools and services for accelerator control systems.
Education
  M.S. Electrical & Computer Engineering, Stony Brook University
Technical Focus
  Controls Architecture
  EPICS & Phoebus
  Distributed Systems
  DevOps, CI/CD, & Infrastructure Automation

## Slide 3: Charge Questions
Are the system requirements sufficiently defined, understood, and documented for this phase of the design?
Do the designs meet the requirements?
Are the interfaces sufficiently defined, understood and documented for this phase of the design?
Are the design analysis, simulations, drawings and specifications, and work plans, sufficient for this phase of the design?
Have technical risks been identified and are mitigation plans adequate for this phase of the design?
Are plans to address ES&H and Quality sufficient for this phase of the design?
Is the overall design maturity sufficient to proceed with the final design phase?

## Slide 4: Outline
Scope
Requirements
Phoebus
Phoebus applications
  Display Builder
  Databrowser
  Alarm Applications
  Logging
Phoebus Architecture
Risks
Path Forward
Summary

## Slide 5: Scope
User-facing tools for control system operation
  Focus on applications used to monitor, operate, diagnose, and document large-scale control systems
Phoebus as the primary application environment
  Cover the integrated Phoebus toolkit, including displays, alarms, archiving, logging, PV tools, and save/restore workflows
Client libraries beyond Phoebus
  Include libraries that bring control system access into other environments and languages
Integration with analysis and engineering workflows
  Discuss use from Python notebooks, MATLAB applications, scripts, and custom tools
Common goal
  Provide flexible, connected interfaces for users to interact with the control system in the environment that best fits their task
Charge #1

## Slide 6: Requirements
Initial versions of the Performance Requirements Documents (PRDs)
  High Level Applications [EIC-SEG-RSI-158]
  Networking & Computing [EIC-SEG-RSI-XXX]
Charge #1

## Slide 7: Control System Architecture
Operator and application layer (Phoebus tools, web tools, HLAs) [EIC-ROD-069]
Middle-layer services (Archiver, Alarm, Olog, ChannelFinder, Save/Restore, Gateway)
Control system layer (EPICS 7 with PVA-first, CA compatibility)
Charge #1-5

## Slide 8: Phoebus
Rich client toolkit for control system applications
  A collection of tools for monitoring, operating, and troubleshooting large-scale control systems
  Provides a unified desktop environment for operators, engineers, and developers
Integrated application framework
  Combines displays, alarms, archiving, logging, PV tools, and save/restore workflows
  Enables applications to share data and operational context automatically
Seamless cross-application workflows
  PV names, values, timestamps, alarm states, archive sources, displays, and logbook entries can move from one tool to another
  Operators can move naturally from alarm investigation, to historical data, to device displays, to logbook documentation
Consistent and extensible user experience
  Shared UI patterns, menus, selections, and context handling reduce operator effort
  Applications interoperate through well-defined interfaces without tight coupling
Scalable, sustainable, and collaborative platform
  Supports modern Java LTS releases, containerized deployment, CI/CD workflows, and microservice-based infrastructure
  Developed collaboratively by facilities worldwide as an open ecosystem for control system tools
Charge #1-5

## Slide 9: Display Builder
editor
runtime
Charge #1,2,4

## Slide 10: Display Builder - editor
WYSIWYG editor
Large Pallet of widgets
Control System Aware
Advanced customization through properties and scripting
Resuable widgets/groups/screens
Simple file format
Charge #1,2,4

## Slide 11: Display Builder - runtime
Live process data with metadata, alarm awareness, units, and precision
Charge #1,2,4

## Slide 12: Web Runtime and Remote Operations
Help support remote operations by bringing OPI screens to the web
.bob files converted to web runtime OPI’s
Charge #1,2,4

## Slide 13: Screen creation
Charge #1,2,4

## Slide 14: Data Browser
Presents live and historical data in one plotting environment
  Cross-channel correlation for diagnosis and post-mortem analysis
  Data export and inspection
  Optimized retrieval
Workflow continuity with display, alarm, and logbook tools
Supports multiple archive providers
Charge #1,2,4

## Slide 15: Alarm Applications
Goals
  Support operator response quality and reduces troubleshooting latency during commissioning and operations
  support configuration and management of Alarm Server behavior (alarm hierarchy, limits, and annunciation rules)
Charge #1,2,4

## Slide 16: Alarm Applications
Alarm clients include
  Tree
    Organized hierarchical view of alarms
  Table
    Fast detection of new, pending, and acknowledged alarms with severity and timestamp context
  Panel
  Annunciator
  Alarm history
    supports post-mortem review and alarm-quality tuning
Charge #1,2,4

## Slide 17: Save and Restore
Save & Restore
  Organized representation of Configurations and Snapshots
  Interface to live, archived, and snapshot data
  Integration with logbook
Charge #1,2,4

## Slide 18: Logbook
Enable users to create and retrieve log entries which document EIC operations, observations, and events.
  Phoebus clients Automatic context capture: Log entries are pre-populated from the active application state.
  Web clients Easy access for quick entry and review
Charge #1,2,4
Notes: Automatic context capture: Log entries are pre-populated from the active application state.
Alarm integration example: Entries created from Alarm tools can initialize with alarming PV(s), alarm severity/state, and timestamp.

## Slide 19: Applications Portfolio
Channel Finder Clients – fast PV search enriched with metadata (IOC host, record type, tags)
PV Utilities –
  Probe: detailed PV introspection
  PV Table: monitor/save groups of PVs
  PV Tree: visualize EPICS record linkages

## Slide 20: Commissioning tools
Tuning and Scans
  Model-assisted scans, optimization loops, and scripted recovery/tuning workflows (HLA.1, HLA.2)
Beam Diagnostics and Optics Correction
  Orbit, tune, trajectory, and optics correction using BPM and response-matrix methods
Model-Based Commissioning
  Online model integration (virtual accelerator / digital twin style) to reduce machine time and risk (HLA.4)
Commissioning tools infrastructure
  Infrastructure/framework needed to build and integrate these tools
  Python and Java client libraries are in development for controls-system and middle-layer service access
Greg White, Murali Shankar SLAC; Ivo List, ESS
corrector = Corrector(deviceName=`FM1G4C02A`)
>> channels = cf.find(deviceName=‘FM1G4CO2A’)
xPos, yPos = corrector.getPositions()
>> xPosPv = cf.find([(deviceName,‘FM1G4CO2A’), (elemField, ‘x’)])
>> yPosPv = cf.find([(deviceName,‘FM1G4CO2A’), (elemField, ‘y’)])
>> caget(xPosPv ) and caget(yPosPv )
corrector.setPositions(xPos=1.23, yPos=3.21)
>> caput(‘SR:C02-MG:G04A{HFCor:FM1} Fld-SP’, 1.23)
>> caput(‘SR:C02-MG:G04A{VFCor:FM1} Fld-SP’, 3.21)
Notes: - **Automated Tuning and Scans** - **Model-assisted scans and optimization loops automate iterative tuning while preserving operator oversight** - **Scripted commissioning workflows support repeatable setup, recovery, and retuning tasks** - **Aligns with HLA requirements for custom beam-physics applications and consistent packaging (F-EIC-CTRL-SW-HLA.1, HLA.2)** - **Beam Diagnostics and Optics Correction** - **Applications support orbit, tune, and trajectory correction using BPM data and response-matrix methods** - **Structured PV data and service interfaces enable machine-wide diagnostics and correction workflows** - **Supports faster fault isolation and reproducible correction studies during commissioning** - **RF and Timing Commissioning** - **Phase alignment, timing synchronization, and LLRF validation workflows are integrated with controls data paths** - **Injection timing and synchronization tools use repeatable scan/verify cycles with archived evidence** - **Interfaces are built on EPICS/PVA communication paths used by commissioning applications (F-EIC-CTRL-SW-HLA.3)** - **Configuration and State Control** - **Save/Restore snapshots capture known-good machine states for controlled studies and rollback** - **Versioned settings and repeatable restore workflows reduce risk during invasive tuning activities** - **Supports operational consistency across shifts and staged commissioning campaigns** - **Operational Traceability** - **Electronic logbook entries, alarm/event context, and archiver history provide auditable commissioning records** - **Post-mortem analysis correlates actions, alarm states, and time-series process data for root-cause studies** - **Improves handoff quality between operations, controls, and physics teams** - **Model-Based Commissioning** - **Online model integration (virtual-accelerator/digital-twin style) reduces machine time and commissioning risk** - **Model/control workflow supports comparison of measured behavior against predicted responses** - **Consistent with requirement to provide interfaces to physics modeling tools (F-EIC-CTRL-SW-HLA.4)** Notes: 1. This slide is intentionally physics-commissioning focused and excludes installation workflow tooling. 2. Keep each workflow tied to traceable evidence (logbook + alarms/events + archiver) to support review and post-mortem analysis. 3. All commissioning applications use EPICS/PVA interfaces and align with HLA requirements in EIC-SEG-RSI-158 Table 4-2. 4. Model-assisted commissioning is a risk-reduction strategy for limited machine-time phases. References: - HLA requirements authority: [supporting-docs/EIC-SEG-RSI-158-Control.Software-Performance.Requirements.Document.txt](../supporting-docs/EIC-SEG-RSI-158-Control.Software-Performance.Requirements.Document.txt) - EPICS software framework moves from controls to physics (paper): [presentations/raw/commissioning-tools/tuzzplm3.pdf](raw/commissioning-tools/tuzzplm3.pdf) - EPICS software framework moves from controls to physics (talk): [presentations/raw/commissioning-tools/tuzzplm3_talk.pdf](raw/commissioning-tools/tuzzplm3_talk.pdf) - High-level physics controls applications for FRIB (phantasy): [presentations/raw/commissioning-tools/tucpr07.pdf](raw/commissioning-tools/tucpr07.pdf) - EPICS decision baseline: [rod/EIC-ROD-EPICS-Control-System.md](../rod/EIC-ROD-EPICS-Control-System.md)

## Slide 21: Phoebus Architecture
Modular framework 🡪 built on Java + JavaFX (no Eclipse RCP)
  Core modules: PV access, VTypes, adapters, logging, jobs
  Core-UI modules: docking, menus, selection services
  Applications: operator-facing tools (Display Builder, Data Browser, etc.)
Jobs & scheduling – run tasks off the UI thread for responsiveness
Connection management – pooled, reusable PV and REST clients
VTypes – canonical value model
  Protocol-agnostic, not tied to memory layout
  Immutable and safe to share
Formula functions – efficient, thread-safe data processing pipelines
Charge #2,4,5
Notes: •Jobs & scheduling – run tasks off the UI thread for responsiveness
•Connection management – pooled, reusable PV and REST clients
•VTypes – canonical value model
•Protocol-agnostic, not tied to memory layout
•Immutable and safe to share
•Formula functions – efficient, thread-safe data processing pipelines
•Selection services – share user-selected data cleanly across applications
•Adapter services – enable runtime integration between loosely coupled apps
•Preferences & layouts

## Slide 22: Phoebus Architecture - Extensibility
Extensible via Java SPI (Service Provider Interface)
  New data sources & protocols (CA, PVA, MQTT, Tango, …)
  Clients for middle-layer services (Olog, elog, …)
New applications
UI extensions (menus, toolbars, context menus)
Charge #
Charge #2,4,5

## Slide 23: Phoebus Architecture – eic product
EIC phoebus product includes site specific
  Applications
  Datasources
  Configurations
  Branding
  Adapters
Address the needs of a particular organization or workflow.
Charge #
Charge #2,4,5

## Slide 24: Phoebus Collaboration
An international collaboration of dozens of research facilites
Phoebus
  ~300 PR’s
  ~100 Issue
Charge #
Charge #2,5

## Slide 25: Risks
Risk RT-6-007-001
  Mitigation: modular, extensible framework enables targeted upgrades with minimized disruption
  Mitigation: multi-lab collaboration spreads maintenance risk and improves response speed to technology changes
Charge #5
Notes: - **Application workflow model is coherent and source-backed**
- **Core application set, middle-layer service model, and architecture direction are defined**
- **Desktop and web usage patterns are established**
- **Complete formal performance characterization under representative load**
- **Finalize subsystem rollout priorities and acceptance evidence**
- **Close unresolved interface and operational ownership items**
- **Validate web-runtime and service assumptions against EIC-specific rollout plans**
- **Are boundaries of the application scope acceptable for this phase?**
- **Which workflows need deeper review before final design?**
- **Which source talk elements stay in the main body versus appendix for the final slide deck?**

## Slide 26: Summary
Phoebus is the primary application environment for EIC operator workflows, with integrated tools for control, diagnostics, and documentation
  Display Builder, Web Runtime, and Data Browser provide a practical path from screen creation to remote operations and post-event analysis
  Alarm, Save/Restore, and Logbook workflows improve operational response quality, repeatability, and traceability
  PV utilities strengthen day-to-day usability through fast discovery, metadata context, and diagnostics support
A modular Java/JavaFX architecture with SPI extensibility supports long-term maintainability and site-specific product composition
Active multi-lab collaboration and targeted risk mitigations position the applications stack for final-design progression